## Slide 1: electronRx Cardio Challenge
Henry Butlin

## Slide 2: The task
Signal processing & feature extraction from 10 raw PPG datasets.
  Cleaning
  Missing data
  …
Compare to expected results & modify strategy if necessary
Discriminate SR & AF
Visualisation
Thinking process rather than full code.

## Slide 3: Signal Processing First approach: FT (C-code)
RAW PPG
Noisy, drifting baseline
bandpass filter & SciPy peak finding *
(see .c file on GitHub)
Improved! But:
Results not a great match to expected
FT can’t handle missing data (see later slide)
* peaks, _ = find_peaks(df.r, height = 0.1, distance = 35)

## Slide 4: Second approach: Python toolkit
SciPy Savitzky-Golay noise filter, polynomial baseline correction & peak find
(Rescaled)
(Rescaled)
RAW PPG
RAW PPG
Better!
Can handle gaps in data
Results closer to expected

## Slide 5: Peak find on raw data?
To see if the signal preprocessing was having a positive effect, I coded my own peak detection program that didn't need filtered data.
This worked by finding the positions of the local maxima within incremented windows of data, and yielded visually correct results.
RAW PPG
RAW PPG

## Slide 6: Missing Data
Some of the raw PPG files were missing rows of data.
As a quick and crude workaround, obtained heart rate was multiplied by the fraction: nexpected/nactual
With more time, small gaps could be filled by maximum entropy interpolation, and larger ones by deep learning models such as recurrent neural networks.
GAP!
nexpected
nactual

## Slide 7: Results
File | HR (exp) | HR (SG, P) | HR (raw)
2022-06-07 09-15-58 | 76.0 | 76.6 | 77.6
2022-06-07 11-04-55 | 56.4 | 56.3 | 55.3
2022-06-07 11-22-35 | 89.3 | 92.0 | 85.6
2022-06-14 09-42-01 | 70.6 | 83.1 | 70.1
2022-06-07 09-51-55 | 88.3 | 87.4 | 88.4
2022-06-14 09-31-19 | 54.3 | 87.0 | 63.7
2022-06-14 12-55-43 | 57.1 | 65.3 | 52.2
2022-06-14 11-07-24 | 74.2 | 79.4 | 73.3
2022-06-14 11-55-02 | 66.4 | 66.1 | 67.1
2022-06-07 10-03-36 | 65.4 | 65.1 | 63.1
My code yields the rMSSD, SDNN, and pNN50, but for simplicity only HR is displayed here
In five cases the filtered results are better than the unfiltered ones – my filtering hasn’t changed information content, but has visually improved the data
I investigated the significant outlier in filtered …
Expected
Processed
Raw

## Slide 8: Non-matching Metrics
The highlighted anomalous value was the only significantly different value
The source of this error appears to stem from counting secondary peaks
(May be clinically significant?)
Could be fixed by a more sophisticated filtering technique or peak detection algorithm (e.g. AMPD*)
*Article link
RAW PPG
RAW PPG
Filtered PPG
Filtered PPG

## Slide 9: Atrial Fibrillation vs Sinus Rhythm
A study conducted in 2020 found that a deep learning approach was successful in detecting AF from raw PPG data.*
Here, the rMSSD, SDNN, or pNN50 metrics could be used as crude differentiators between AF and SR.
As AF is characterised by irregular heartbeats, it seems plausible that a larger range of heartbeat intervals would imply AF.
A brief visual inspection of the raw PPG waveforms might also be an effective initial screening method.
*Article link

## Slide 10: Visualisation
Examples of ways to visualise and verify these results.
In some cases one or more of these plots showed something was going wrong (e.g. peak vs time was non-linear), which would be useful for future debugging.